## Slide 1
The Mobile System S_JEP-12495-97 György Györök Kandó Kálmán Technical College Institute for Computer Technology
Notes: I,w choiche a verry fine pice of coke of the network computing it is the „mobile systems”.
Until my work was more and more clearly it is one relaitvly heawy food.
And so my work consist of two differebt deep
part.
First is frame in wich I wouldlike dcisison the frame in wich I can moving.
The scond part is a wellfilled part of this cover.

## Slide 2
The Cell of Network
Notes: Basicaly each device on network heve two function: onhand it’s one data source and otherhand is it one data drain.
For this both function necessaries one transmitter and one receiver. Shortly togeather this two functuion is it one transiever. This transiever simplex comminication can due with other network device. The simplex means the onetimes the down datastream can due, and other time the up stream.

## Slide 3
The Mobile System
· Infrastructures
· Services
· Applications
· Protocols
Notes: I try to classification this topics according the:
Let’s start on the tree in green colour!

## Slide 4
The Infrastructures (Wireless networking)
· Radio frequency
· Light (Laser, Infra)
· Others (Mixed)
Notes: The infratructures (in important order) today mens the ...
The light communication not verry importantin in normal application but in interferenced industrial envairoment may be usful.
Forexample the mixed methode is one circel wire line, as one antennas (this is the down stream) and the upstream is one infra transmitter.

## Slide 5
Radio frequency Communication
Ordinary 60 kHz - 6 GHz
Satellite (2GHz-)
Point to Point (Cable, Laser)
Cellular
Notes: The spectrum of the ability radio frequency communication not coherent.
Enough if we think for the broadcasting tv, aerotrafic, the ordinary art of communication.This special bands are occupieded, because mor thin the usable bandwitdh.

## Slide 6
The Digital Radio Cannel
EARs
Data
Data
Notes: You can see one classical radio cannal.
The distance, the communications speed, the transmiter’s power and the receiver’s sensibiliti, the art of modulation are a verry complex thinks. Every part of this depend from eachother.

## Slide 7
The Comparison of Modulation Techniques 1
Notes: In the next any slides i try to comparison the modulation techniques.
In this two columns can yo see the transfer speed and the ability noise ration.

## Slide 8
The AM Techniques
OOK
OOK DSB-SC
QAM, QPSK
Notes: Its the basic equals wihch write down the
AM.

## Slide 9
The Comparison of Modulation Techniques 2
Notes: In this slide you can see this quantities at FM.
Frequency Shift Keying
Continous Phase Frequency Shift Keying
Fiktive Phase Frequency Shift Keying
Modified Shift Keying

## Slide 10
The FM Techniques
Notes: Its the basic equals of the FM

## Slide 11
The Comparison of Modulation Techniques 3
Notes: In this slide can you see the two better solutions of datatransfer in noisi environment.
Its the eight-, and sixteen ary phase shift modulation.

## Slide 12
The PSK Techniques
ai
Ti
Location of Signal
Notes: This slide can sggest the algorytm of sixteen ary PSK modulation.

## Slide 13
Conclusion
The battle neck is (with enough transfer speed) is the bandwidth
Solution the: Spread of the Spectrum

## Slide 14
SPREAD SPECTRUM
ADVANTADES:
· Low power spectral density
· Interference limited operation
· Privacy due to unknown random codes
· Reduction of multi-path effects
· Random access possibilities
· Good anti-jam performance
Notes: What is the advantages of Spread Spectrum?
In the next slides you can see detail this arguments.

## Slide 15
The Low power spectral density
Notes: Basicaly this means the over harmonic ration, the interference with narrow band communications is not too much.
Becaause the spreaded signal power is near that of gaussian noise levels.

## Slide 16
Interference limited operation
Notes: An SS receiver uses a locally generated pseudo noise code and a receiver correlator to separate only the coded information from all possible signals.
The correlator does not respond to man made, natural or artificial noise or interference. It responds only to SS signals with identical matched signal characteristics and encoded with the identical pseudo noise code.

## Slide 17
Anti-jam performance
Notes: Good anti-jam performance, because of the difficulty to jam or detect spread spectrum signals.
Thet first applications were in the military field.

## Slide 18
Multi-path effects
Reflection
Dispersive
Refractive
Transmitter
Receiver
Notes: The short height of the receiving antennas, the natural and human-made structures surrounding them would generate the multipath fading on the received signal. A time delay spread exists due to the time dispersivity and distorsion.

## Slide 19
The Spread Spectrum Modulation System
Data
Notes: CDMA receivers, separate communication channels by a pseudo-random modulation that is applied and removed in the digital domain. Multiple users can therefore occupy the same frequency band.
Spread spectrum modulation, uses a transmission bandwidth many times greater than the information bandwidth.

## Slide 20
The Art of Spread Spectrum
· FH frequency hopping
· CDMA code division multiply access
· TDMA time division multiply access
· CSMA code sensitive multiply access
· DDCA distributed dynamic channel assignment

## Slide 21
The Spectrum of FH
Notes: When applying Frequency Hopping, the carrier frequency is 'hopping' according to a unique sequence (an FH-sequence of length). In this way the bandwidth is increased by a factor (if the channels are non-overlapping):

## Slide 22
The Frequency Hopping
Notes: The process of frequency hopping is illustrated on this slide too.
A disadvantage of Frequency-Hopping is that obtaining a high processing-gain is hard. There is need for a frequency-synthesiser able perform fast-hopping over the carrier frequencies.

## Slide 23
The Frequency Hopping
Notes: Implementation must be easily implemented and reproducible; because the same genera-ting process must be used at the transmitter (for spreading); and at the receiver for despre-ading.

## Slide 24
The FH Receiver
Traansmission
Channel
Data
Notes: The signals generated at the receiver must be perfectly synchronised with the timing of the received transmission.

## Slide 25
CDMA 1
The jamming effects are reduced because jamming-signal in the radio channel will be spread before data-detection is performed
The problem with applying Direct Sequence spreading is the Near-Far effect
Notes: The next art of spreading of the frequency is the code division multiplie acess.

## Slide 26
CDMA 2
The data signal is multiplied by a Pseudo Random Noise Code (PN code)
This results in low cross-correlation values among the codes and the difficulty to jam or detect a data message
Standard of binary PN-codes: [Gol67, HdV71, Roe77,Gla92, YLF94, SOSL85a,Hol82,Dix84,PSM82, SH85]
Notes: Its the next some advantages of CDMA.

## Slide 27
Hybrid System DS-(F)FH
Notes: The DS/FH Spread Spectrum technique is a combination of direct-sequence and frequency-hopping. One data bit is divided over frequency-hop channels (carrier frequencies). In each frequency-hop channel one complete PN-code of length is multiplied with the data signal

## Slide 28
The Direct Sequence
Notes: As the FH-sequence and the PN-codes are coupled, an address is a combination of an FH-sequence and PN-codes. To bound the hit-chance (the chance that two users share the same frequency channel in the same time) the frequency-hop sequences are chosen in such a way that two transmitters with different FH-sequences share at most two frequencies at the same time (time-shift is random).

## Slide 29
The Direct Sequence
Notes: The sequences must be build from 2-leveled numbers. The codes must have a sharp (1-chip wide) autocorrelation peak to enable code-synchronisation. The codes must have a low cross-correlation value, the lower this cross-correlation, the more users we can allow in the system. This holds for both full-code correlation and partial-code correlation.

## Slide 30
Spread-spectrum receiver
Data
Notes: This receiver more complicitier as the earlier.
PLL is verry important. In more application this loop is the DPLL.

## Slide 31
The Generation of PN-codes
Notes: The generation of the PN ccccodes is relatively easy, a number of shift-registers is all that is required. For this reason it is easy to introduce a large processing gain in Direct-Sequence systems.
When the length of such a shift-register is n, the following can be said about the period of the above mentioned code-families.
In direct-sequence systems the length of the code is the same as the spreading-factor with the consequence.

## Slide 32
The QPSK Transmitter
Data
Traansmission
Channel
Notes: To avoid any dependence on carrier phase, it could be convenient to put in consideration the QPSK spreading modulator and corresponding demodulator. In this scheme, the input data are still biphase modulated. In QPSK systems, it is assumed that: The receiver is tracking the transmitted carrier perfectly.

## Slide 33
The QPSK Receiver
Data
Traansmission
Channel
Notes: The inphase (I) and quadrature (Q) pseudorandom sequences are independent; which means, that either the generators are the same, or the initial vectors are separated by a randomly chosen offset). It can be shown that the first and second-order statistics for QPSK modulation by pseudorandom sequence are exactly the same as those for BPSK modulation.

## Slide 34
The Spectrum of QPSK
Notes: Spectrum of QPSK.

## Slide 35
The Gold Code
Notes: The Gold-code sets can be roughly divided into two classes: orthogonal codes and non-orthogonal codes.

## Slide 36
The Gold Code Generator
Clocck
Gold
Code
Notes: The first category, is the called shift-register sequences [Gol67, Roe77, SP80].

## Slide 37
The Walsh Hadamard Codes
Notes: Walsh-sequences have the advantage to be orthogonal, in this way we should get rid of any multi-access interference.
The codes do not have a single, narrow autocorrelation peak. The spreading is not over the whole bandwidth, instead the energy is spread over a number of discrete frequ-ency-components.

## Slide 38
The BPSK Transmitter
Data
Traansmission
Channel

## Slide 39
The BPSK Receiver
Data
Traansmission
Channel

## Slide 40
The Spectrum of BPSK

## Slide 41
The TH Receiver
Traansmission
Channel
Data
.....
Notes: Time-Hopping (TH) is also possible to make use of combinations of them. An overview of the receeiver

## Slide 42
The Application of the Radio frequency Communication
CN
PCN
DTV, DAB
GPS
Notes: Heve some well knoling application in mobile system:

## Slide 43
The Trend
More efficiency Code
Compress Techniques
Code generation by Firmware
Integrated Modules

## Slide 44
The Integrated Modules
Notes: Texas

## Slide 45
Conclusion and Future Work
The ready work about (from here view) 120-150 slides
Test in postgraduate course
Iteration

## Slide 46
The Light Communication

## Slide 47
The Optical Communication
Laser in ear point to point in closed room
Infra in closed room

## Slide 48
The Ability Modulation in Optical Communication
Pulse-frequency Modulation (PFM)
Frequency-shift Code (FSC)
Frequency-shift Keying (FSK)
Modified Frequency-shift Keying (MFSK)
Phase-shift Keying (PSK)
Modified Phase-shift Keying (MPSK)
Delayed Modified Phase-shift Keying (DMPSK)
Phase-delayed Keying (PDK)
Modified Phase-delayed Keying (MPDK)

## Slide 49
The Laser PFM Cannel

## Slide 50
The Optical PFM Cannel
TD=1/fo
f=frequency deviation
M=avalanche detector multiplication factor
PSO=peak receiver optical power
tr=pulse rise time at the limiter input
B=postdetection baseband noise bandwidth
ieff2=receiver mean square noise current
r=responsivity

## Slide 51
The Infra Receiver
Data

## Slide 52
The Output of biphase Infra Receiver

## Slide 53
Thank you for Attention The End

## Slide 54
The Satellite Communication